## BEFORE START

Fire Extinguisher		CHECK

O2 Pressure & Masks		CHECK

Overhead Panel		All OFF

EPS				TEST/ARM

L & R Circuit Breakers		CHECK

Parking Brake			SET

Lower Panel Switches		CHECK

LH/RH FUEL PUMPS		TEST

Inertial Separator		OPEN

ECS/Pressurization		OFF

Pedestal Controls		CHECK

Firewall Cutoffs			CHECK

Battery Switch			ON

Landing Gear			3 GREEN

Master/Caution			RESET

Fire Warning			TEST

Lamps				TEST

EIS				TEST

Fuel Quantity			RESET

Beacon				ON

## BATTERY START

START Switch			ON

Oil Pressure			CHECK

Ng				STABLE >13

Condition Lever			GROUND IDLE

ITT				Monitor; <800

Ng				Stable; >60

PROP				>950 rpm

### GPU START (Battery Switch “ON”)

GPU				CONNECT; ON

EXTERNAL Power		ON

START Switch			ON

Oil Pressure			CHECK

Ng				STABLE >13

Condition Lever			GROUND IDLE

ITT				Monitor; <800

Ng				Stable; >60

EXTERNAL Power		OFF

GPU				DISCONNECT

### AFTER START

GEN 1				ON; AMPS <200

GEN 2				ON

AVIONICS 1 & 2			ON

INVERTER			Set GEN

ECS				ON

Environmental Controls		As Needed

Cabin Lights			SET

AHRS 1 & 2 			CHECK

FLAPS				SET 15 Degrees

Trim				Check 4/Set 3

Autopilot				TEST

Pusher				TEST

EGPWS				TEST

CAWS/EIS/MFD			CHECK

ATIS				CHECK

Clearance			Obtain; Enter

#### BEFORE TAXI CHECK

Exterior Light			CHECK

EIS				CHECK

FLAPS				CHECK

Flight Controls			CHECK

Altimeter				CHECK

Avionics/X-Ponder		CHECK

Pressure Controller		SET

De-Ice				TEST

Probes & Windshield		ON

Battery Amps			< 15

RADAR				TEST

#### LINE UP CHECK

F-A-T F-L-Y (flaps-and-trim; flight idle; lights; YD)

#### TAKE OFF

Gear				UP

Yaw Damper			ON

Flaps				UP

Airspeed				Monitor

Power				Set

Inertial Separator		CLOSE

#### CLIMB CHECK

Pressurization			CHECK rate

Recog light			OFF >10,000 agl

Altimeter				Reset >18,000

#### CRUISE CHECK

SEAT BELTS			OFF

Ice Protection			As Required

POWER				SET

Data				Record

#### Take Off Flaps

15		Vrot = 79

- Vrot = 73

# Vx		110

Vy		120

FLAPS	Vfe KIAS	Vref KIAS 	  Vref (ice) KIAS

0		-----------	    118		134

15		163		      98		108

30		130		      89		 NR

40		130		      84		 NR

WEIGHT		BEST L/D		Va

9921				114		158

9500				112		155

9000				110		145

8400				106		143

7900				103		141

7500				100		137

7000				  97		133

6600				  93		129

#### DESCENT

Vmo/Mmo			WATCH!!

Presurization			SET

Ice Protection			SET

Transition Level			18,000’

Recog Lights			ON below 10000’ AGL

BEFORE LANDING

Inertial Seperator		OPEN

Landing Gear			DOWN <176 KIAS

Lights				AS REQUIRED

Flaps				SET <163 KIAS

Yaw Damper			OFF

Rudder Trim			CENTER

AOA Indicator			MONITOR

AFTER LANDING

Ground Idle			SET

Flaps				15/0

ECS				OFF

De-Ice				OFF

External Lights			As Needed

Trim				Reset 3

SHUTDOWN

Cool & Heat			OFF

#### Lights				OFF

Overhead Panel			All OFF

ITT				Stabilize

Conditioner Lever		CUT OFF

Inertial Separator		CLOSE

Pax O2				OFF

O2 Main				OFF

Battery				OFF < 8% Ng

Gust Lock			IN

POST FLIGHT CHECK

Headset Battery			OFF

Parking Brake			As Needed